## Slide 1: Titolo presentazione sottotitolo
Milano, XX mese 20XX
HANDY: a wireless sensorized glove
for ASL fingerspelling gesture recognition
Ilaria Crupi
Arianna De Vecchi
Diana Nigrisoli
Professor: Pietro Cerveri
Tutor: Matteo Rossi
July, 26th 2023

## Slide 2
Project 04 - Crupi, De Vecchi, Nigrisoli
Project Aim
Hardware
Firmware
Acquisition Protocol
Software
Contents
Handy

## Slide 3
Develop a smart glove able to teach the American Sign Language (ASL) to people who are unfamiliar with it.
Project Aim
Hardware
Firmware
Acquisition Protocol
Software
Project 04 - Crupi, De Vecchi, Nigrisoli
Hearing loss affects more than 1.5 billion people, nearly 20% of the global population [1].
This communication barrier adversely affects the lives and social relationships of these people.
Provide ASL education in the form of a game.
[1] https://www.who.int/health-topics/hearing-loss. Accessed on 23 July 2023

## Slide 4
Hardware
Firmware
Acquisition Protocol
Software
5 flex sensors: one on each finger
Project 04 - Crupi, De Vecchi, Nigrisoli

## Slide 5
Hardware
Firmware
Acquisition Protocol
Software
5 flex sensors: one on each finger
2 force sensors: between index and middle finger and under the thumb
Project 04 - Crupi, De Vecchi, Nigrisoli

## Slide 6
Hardware
Firmware
Acquisition Protocol
Software
5 flex sensors: one on each finger
2 force sensors: between index and middle finger and under the thumb
3-axis accelerometer
Project 04 - Crupi, De Vecchi, Nigrisoli

## Slide 7
Hardware
Firmware
Acquisition Protocol
Software
5 flex sensors: one on each finger
2 force sensors: between index and middle finger and under the thumb
3-axis accelerometer
HC05 Bluetooth module
Project 04 - Crupi, De Vecchi, Nigrisoli

## Slide 8
Hardware
Firmware
Acquisition Protocol
Software
5 flex sensors: one on each finger
2 force sensors: between index and middle finger and under the thumb
3-axis accelerometer
HC05 Bluetooth module
PSoC microcontroller
4.5V battery + 3.3V LDO
Yellow LED
Round Switch
Project 04 - Crupi, De Vecchi, Nigrisoli

## Slide 9
Hardware
Firmware
Acquisition Protocol
Software
Project 04 - Crupi, De Vecchi, Nigrisoli
Tests with breadboard
PCB Design

## Slide 10
Hardware
Firmware
Acquisition Protocol
Software
Project 04 - Crupi, De Vecchi, Nigrisoli
PCB Production
Drill and soldering

## Slide 11
Hardware
Firmware
Acquisition Protocol
Software
Project 04 - Crupi, De Vecchi, Nigrisoli
3D printed case and final implementation

## Slide 12
Firmware
Acquisition Protocol
Software
Project 04 - Crupi, De Vecchi, Nigrisoli
ASL gesture
Microcontroller
Accelerometer
Force sensors
Flex sensors
Sensorized glove
Custom cables
PCB
UART
MUX
(7 channels)
VFD
ADC
Timer
I2C
read ACC
10 samples avg
Handy

## Slide 13
Acquisition Protocol
Software
Chart: Recordings N° = 79
| Male | Female
Recordings | 11 | 68
Chart: Subjects N° = 15
| Male | Female
Recordings | 6 | 9
Project 04 - Crupi, De Vecchi, Nigrisoli
For every subject:
Perform all the alphabet
Do 3 more gestures:
‘open’ Hand fully open with the back facing the subject
‘closed’ Hand completely closed
‘dummy’ Hand fully open with palm facing upwards
Repeat at least two times

## Slide 14
Project 04 - Crupi, De Vecchi, Nigrisoli
Software - ML
A Machine Learning approach for hand gestures classification was developed
Data Scaling
Classification models
Analog sensors
Pseudo min-max standardization:
Accelerometer
MinMaxScaler fitted on the training set
K Nearest Neighbours
Classification Tree
Random Forest
Adaboost
Logistic Regression
Multilayer Perceptron

## Slide 15
Project 04 - Crupi, De Vecchi, Nigrisoli
Software - ML
The best model turned out to be Random Forest
'criterion': 'entropy’,
'max_depth': 12,
'min_samples_leaf': 5,
'min_samples_split': 12,
'n_estimators': 150
F1 score | Train set | Test set
 | 0.900 | 0.835

## Slide 16
Project 04 - Crupi, De Vecchi, Nigrisoli
Software - ML
The best model turned out to be Random Forest
Easily confused
Well classified

## Slide 17
Project 04 - Crupi, De Vecchi, Nigrisoli
Software – GUI
Log-in
Menu
Statistics
Game
Calibration
The GUI is designed as a video game that tests the user’s ability in ASL spelling.
It is composed of 5 windows:

## Slide 18
Project 04 - Crupi, De Vecchi, Nigrisoli
Software – GUI
Log-in
Menu
Automatic connection to COM when starting the game
Statistics
Log out
Log-in with username
If there is no username, it gives an error

## Slide 19
Project 04 - Crupi, De Vecchi, Nigrisoli
Software – GUI
Game
Random letter provided when pushing «Start»
10 seconds to make the right gesture
The ML model gives a prediction on the letter performed. If the prediction matches the actual letter, the score increases.

## Slide 20
Project 04 - Crupi, De Vecchi, Nigrisoli
Software – GUI
Calibration
Calibration consists in a 2-step procedure:
Hand fully open
Hand completely closed
Calibration must be performed at least once. The device acquires and saves the calibration data into a csv file specific for each user.

## Slide 21
Project 04 - Crupi, De Vecchi, Nigrisoli
Software – GUI
Statistics
Total Score Chart allows the user to analyze the performance among different rounds (days)
Global Performance Bar Chart shows the percentage of success for each letter

## Slide 22: Thank you!